## Slide 1: Quick Start to Cadsoft Eagle
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/quick-start-to-eagle
Hackware v1.7 (27 April 2016)

## Slide 2: About Eagle
Since 1988 - present
Made by CadSoft Computer GmbH
Commonly used by makers
  Adafruit + Sparkfun + Arduino
Extensive library support
Free “Lite” version
  Non-commercial use
  Max 2 copper layers
  100 x 80 mm board size
To exceed limitations: http://www.cadsoftusa.com/eagle-pricing/
Multi-platform: Windows, Mac, Linux
Saved as XML (ASCII) files, great for version-control

## Slide 3: PCB Design/Manufacturing Workflow
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly

## Slide 4: 1. Establish project requirements
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Switch ON/OFF LED
Powered from coin cell

## Slide 5: 2. Acquire parts and prototype
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
5mm red LED
330ohm resistor
Switch
CR2032 battery holder

## Slide 6: 3a. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Schematic defines connections between components
Open Eagle and add external libraries
Import libraries. (Not shown)
  Locate the libraries folder I have provided
  Drag-and-drop the *.lbr files one by one into Eagle Control Panel Libraries folder
  Right-Click on Libraries Folder -> Use all

## Slide 7: 3b. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Create and save schematic file (part and connection layout)
Create a folder on desktop “quick-start-to-eagle”
Create new schematic *.sch: File -> New -> Schematic
Save schematic

## Slide 8: 3c. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Add components
CR2032 battery holder
  battery -> CR2032H
Switch
  switch-dil -> SD4-01
Resistor
  resistor -> R-US_ -> R-US_0207/10
  2mm diameter, 7mm length, 10mm lead length
5mm Red LED
  led -> LED -> LED5MM

## Slide 9: 3d. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Maneuvering and layout
Zoom with scroll-wheel
Click-drag middle mouse button to move sheet
Rotate components
  Choose Move command
  Click component “+” sign then right-click
Define component value if needed
  Right-click component -> Value
Delete object with trash icon
Wiring
  Use “Net” command
  Link components together
  Hover mouse just overlapping the contacts
  Press “Alt” increased precision key if wire cannot overlap
  Left-click to set and also to change direction

## Slide 10: 4. Run electrical check (ERC)
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Tests if your wiring has been done properly
Not foolproof but usually good enough to detect weird or missing connections
Run ERC regularly, assign to shortcut key. Options -> Assign
Correct ALL errors
Inspect all warnings
  Correct if needed
  Ignore if you are sure
  I discourage approving

## Slide 11: 5a. Design board: place parts & wiring
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Create and save board file (board layout)
File -> Switch to board
Initial board configuration
  Adjust grid settings to mm as shown.
    View -> Grid
  Create keyboard shortcuts for commonly used functions.
    Options -> Assign
    Not case-sensitive
    End with “;”
  Enable Vector font
    Options -> User Interface
    Tick Always vector font
    Tick Persistent
CAM Processor can only convert vector fonts into Gerbers properly.
See: http://www.cadsoftusa.com/training-service/faq/#c95

## Slide 12: 6a. Setup/run design rule check (DRC)
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Design rules provided by fabricator to check if your PCB adheres to requirements
Download PCB fabricator DRU, in this case Elecrow
http://www.elecrow.com/10pcs-2-layer-pcb-p-1175.html
http://www.elecrow.com/download/Elecrow_PCB_eagle_rule.zip
*I use Elecrow as a learning example here but it does not mean I endorse this company in any way.

## Slide 13: 6b. Setup/run design rule check (DRC)
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Load DRU file just once
Press “check” to check your board or use keyboard shortcut
Rectify all errors

## Slide 14: 5b. Design board: place parts & wiring
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
General board steps
  Adjust board size to your requirements eg: 99mm x 49mm (check fabricator price point)
  Place ground/power plane on Top layer using polygon function. 1mm away from edges to ease future resizing. Set polygon name.

## Slide 15: 5c. Design board: place parts & wiring
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
General board steps
  Component placement order
    Place mounting holes
    User-facing components, like USB connectors, switches and LEDs
    Large components
    Everything else
  Wiring order (Trace width usually the size of the solder pads)
    Wire high-speed connections, avoid using vias
    Wire power connections with wider traces
    Wire everything else
  Execute DRC check and rectify if needed
  Silkscreen placement order (don’t overlap with any holes/vias/parts)
    Smash component & adjust part designators if required to minimise confusion
    Add descriptive text to certain areas to silkscreen
    Add PCB description/revision
  Miter corners
  Make sure Ratsnest gives “Nothing to do”
Tips
  Execute Ratsnest to recalculate remaining airwires’ position as much as possible after every operation
  Run DRC after you make every change to catch problems earlier
  Wire at 45 degree angles to reduce signal reflection

## Slide 16: 8. Use CAM file to generate Gerbers
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Gerber files
  2D vector format used by PCB fabricator to make PCBs for you
CAM file provided by fabricator to help you generate Gerber layer files
Download PCB fabricator’s CAM processor, in this case Elecrow
http://www.elecrow.com/10pcs-2-layer-pcb-p-1175.html
http://www.elecrow.com/download/Elecrow_Gerber_Generater_DrillAlign.zip
Use the correct CAM file according to number of layers like 2 layers
Open CAM Processor: File -> CAM Processor
Once in CAM Processor, load the CAM job as shown below
Once you are done, click “Process Job”

## Slide 17: 9. Zip up relevant Gerber files
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
See what files are required by the PCB fabricator
Elecrow’s requirements:
Go to saved folder and zip up the required files
Rightfully you should inspect your Gerber files for potential mistakes using software/websites like:
  GR-Prevue: http://www.graphicode.com/GC-Prevue_Gerber_Viewer
  http://circuitpeople.com/
  http://mayhewlabs.com/webGerber/
  But so far I don’t have any problems so I usually skip the Gerber file check step

## Slide 18: Questions?